## Slide 1: Chapter Two Basic Configuration
Cheru H.

## Slide 2: Outline
Required Resources
Part I: Set Up the Topology and Initialize Devices
Part II: Configure Devices and Verify Connectivity
Part III: Configure Remote (SSH)

## Slide 3: Required Resources
Packet tracer
1 Router
2 Switch
4 PCs

## Slide 4: Part I: Set Up the Topology and Initialize Devices

## Slide 5: Cont’d…
  Cable the network as shown in the topology.
    Attach the devices as shown in the topology diagram, and cable as necessary.
    Power on all the devices in the topology.
  Initialize and reload the router and switch.
Note: Appendix A details the steps to initialize and reload the devices.

## Slide 6: Part II: Configure Devices and Verify Connectivity
  Configure the PC interfaces.
    Configure the IP address, subnet mask, and default gateway settings on all PC.
  Configure the router.
    Console into the router and enable privileged EXEC mode.
Router> enable
Router#
    Enter into global configuration mode.
Router# config terminal

## Slide 7
    Assign a device name to the router.
Router(config)# hostname R1
    Disable DNS lookup to prevent the router from attempting to translate incorrectly entered commands as though they were hostnames.
R1(config)# no ip domain-lookup
    Require that a minimum of 10 characters be used for all passwords.
R1(config)# security passwords min-length 10
Besides setting a minimum length, list other ways to strengthen passwords.

## Slide 8
    Assign cheru12345 as the privileged EXEC encrypted password.
R1(config)# enable secret cheru12345
    Assign haile12345 as the console password, establish a timeout, enable login, and add the logging synchronous command. The logging synchronous command synchronizes debug and Cisco IOS software output and prevents these messages from interrupting your keyboard input.
R1(config)# line con 0
R1(config-line)# password haile12345
R1(config-line)# exec-timeout 5 0
R1(config-line)# login
R1(config-line)# logging synchronous
R1(config-line)# exit
R1(config)#
For the exec-timeout command, what do the 5 and 0 represent?

## Slide 9
    Assign haile12345 as the vty password, establish a timeout, enable login, and add the logging synchronous command.
R1(config)# line vty 0 4
R1(config-line)# password haile12345
R1(config-line)# exec-timeout 5 0
R1(config-line)# login
R1(config-line)# logging synchronous
R1(config-line)# exit
R1(config)#

## Slide 10
    Encrypt the clear text passwords.
R1(config)# service password-encryption
    Create a banner that warns anyone accessing the device that unauthorized access is prohibited.
R1(config)# banner motd #Unauthorized access prohibited!#

## Slide 11
    Configure an IP address and interface description. Activate both interfaces on the router.
R1(config)# int g0/0
R1(config-if)# description Connection to s2
R1(config-if)# ip address 192.168.10.1 255.255.255.0
R1(config-if)# no shutdown

## Slide 12
R1(config-if)# int g0/1
R1(config-if)# description Connection to S1
R1(config-if)# ip address 192.168.20.1 255.255.255.0
R1(config-if)# no shutdown
R1(config-if)# exit
R1(config)# exit
R1#

## Slide 13
    Set the clock on the router; for example:
R1# clock set 17:00:00 18 Feb 2013
    Save the running configuration to the startup configuration file.
R1# copy running-config startup-config
Destination filename [startup-config]?
Building configuration...
[OK]
R1#

## Slide 14: Verify network connectivity.
  Test Verify network connectivity. Ping

## Slide 15: Configure the router for SSH access.
    Enable SSH connections and create a user in the local database of the router.
R1# configure terminal
R1(config)# ip domain-name CCNA-lab.com
R1(config)# username admin privilege 15 secret haile12345
R1(config)# line vty 0 4
R1(config-line)# transport input ssh
R1(config-line)# login local
R1(config-line)# exit
R1(config)# crypto key generate rsa modulus 1024
R1(config)# exit

## Slide 16: Question